## Slide 1: PC Hardware Essentials
Chapter 2:
Electricity and Power

## Slide 2: Common Electrical Terms
Current
  Flow of electricity
Circuit
  Specific path, loop electricity flows along
Power
  Amount of work current can produce
Resistance
  Quality of impeding flow of electricity
Insulator
  Device or material offering resistance

## Slide 3: Common Electrical Terms
Conductor
  Device or material allowing flow of electricity
Continuity
  Describes existence of complete, working circuit
Capacitor
  Device for storing electrical charge
Resistor
  Device used to impede flow of electricity

## Slide 4: Common Electrical Measurements
Amps
  Current’s strength or rate of flow
Ohms
  Conductor’s resistance to electricity
Volts
  Electrical pressure (potential) in circuit
Watts
  Electrical power in circuit range
Calculating voltage and power
  Voltage = Current * Resistance
  Power = Voltage * Current

## Slide 5: Comparing Electrical Current to Water Flow

## Slide 6: Types of Current
AC (alternating current)
  Current changes directions from positive to negative
  60 times per second = 60 Hz
  Provided by power companies
DC (direct current)
  Constant flow from negative (hot) charge to positive (ground) charge
  Type of power used in PCs

## Slide 7: Multimeters
Main components
  Digital or analog display
  Two probes
    Positive (red) probe
    Negative (black) probe
  Function selector switch
    Select function
    Select range of values expected
      E.g. 3V – 12V, 105V-125V

## Slide 8: A Digital Multimeter

## Slide 9: Measuring Voltage
Set function selector to measure AC (or DC) voltage
Choose voltage range
  Usually 20V or lower
Hold black (negative) probe to ground point on circuit
Hold red (positive) probe to hot point on circuit

## Slide 10: Measuring Voltage

## Slide 11: Measuring Resistance
Ensure circuit is not powered
Set function to ohms and set appropriate range
Touch probes to two metal points
Multimeter should give signal (buzz or beep, etc.) to indicate continuity

## Slide 12: Measuring Resistance

## Slide 13: Measuring Current

## Slide 14: Electrostatic Discharge (ESD)
Occurs when two objects of dissimilar charge come in contact with one another
PC electrical components use 3V – 5V
PC circuits can be destroyed by 30V
Small ESD charge: 3,000V
To protect against ESD:
  Antistatic wrist strap
  ESD mats
  Antistatic bags for parts
  Humidity control
  Antistatic spray

## Slide 15: Connecting an Antistatic Wrist Strap

## Slide 16: Using an ESD Mat

## Slide 17: Power Problems
Two types of damage to PC by electrical forces
  Catastrophic damage
  Degradation
Three main classes of power problems
  Power quality problems
  Power overage problems
  Undervoltage power problems

## Slide 18: Power Problems
Power quality problems
  Power fluctuations
  Electromagnetic interference (EMI)
  Radio frequency interference (RFI)
Power overage problems
  Spikes
  Surges
Undervoltage power problems
  Sags
  Brownouts
  Blackouts

## Slide 19: Power Problem Solutions
Line conditioners
  Eliminate noise, most EMI, RFI
  Produce “perfect” 110V/60Hz power
Surge protectors
  Metal oxide varistor (MOV) takes hit from voltage spikes
  Characteristics
    MOV clamping speed, voltage
    Energy absorption (Joules)
    Line conditioning
    Protection indicators

## Slide 20: Power Problem Solutions
Backup power supplies
  Keep power at 110V
  Two types
    Standby power supply (SPS)
      Switches to battery when line voltage drops below cutover threshold
    Uninterruptible power supply (UPS)
      Power run constantly from outlet to battery and then to PC

## Slide 21: Uninterruptible Power Supply (UPS)

## Slide 22: Power Supplies
Rated in watts
Provide standard voltages to motherboard and drives (+5V, +12V, -5V, -12v, +3.3V)
Carry lethal amounts of current
Components include:
  Power cord
  Pass-through connectors
  Power switch
  110/220V selector switch
  Power supply fan

## Slide 23: Power Supply

## Slide 24: Power Supply Components

## Slide 25: Power Supply Form Factors
Power supply must match:
  Form factor of case
  Motherboard power requirements
Power supply form factors
  Older form factors: AT, Baby AT, LPX
  ATX (NLX)
    Uses single 20-pin P1 motherboard connector
    Soft-power feature
  SFX (mini or micro ATX)
    Smaller form factor
  ATX 12V
    Additional 4-pin 12V connector

## Slide 26: Power Supply Form Factors

## Slide 27: Power Supply Connectors
Floppy drive connectors (Berg connectors)
Standard peripheral power connectors (Molex connectors)
Motherboard connectors
  AT system connectors: P8/P9
  ATX system connectors:
    P1 (20-pin or 24-pin)
    Auxiliary power connector (6-pin Molex)
    ATX 12V (P4) connector
PCI Express connectors
SATA drive connectors
Fan connectors

## Slide 28: Floppy Drive Connector (Berg)

## Slide 29: Standard Peripheral Power Connector (Molex)

## Slide 30: P8/P9 Connectors

## Slide 31: ATX 20-pin P1 Connector

## Slide 32: SATA Drive Connector

## Slide 33: Replacing a Power Supply
Unplug PC power
Open case, disconnect all PSU connectors
Remove mounting screws, lift PSU out
Ensure new PSU voltage level set
Insert PSU, reattach with mounting screws
Reconnect to motherboard, drives, fan, etc.
Replace case cover and power cord
Power PC, verify fan is on and PC, drives functioning

## Slide 34: Installing the ATX System Connector

## Slide 35: Maintaining and Upgrading Power Supplies
Be alert to any signs heat is not being dissipated by power supply fan or case fans
Keep PC closed to allow air flow and cooling
Some component upgrades (e.g. SATA drives, powerful CPUs) may require upgrading power supply
  Power supply should provide 10 % more than power requirements of all components

## Slide 36: Troubleshooting Power Supplies
Common power problems
  No power when power button pressed
    Power cord not pushed in
    Front panel power switch connector to motherboard not connected
    Power supply may have own power switch which is turned off
  Computer powers on, then powers down
    CPU fan problem
  Loud bang, smoke at back of case
    Power supply set to wrong voltage

## Slide 37: Troubleshooting Steps
Ensure PSU receiving power
  Is power supply fan on?
  Check connections with power cord, power strips, outlet
Ensure voltage switch set correctly
Check connections to motherboard

## Slide 38: Summary
Power supply converts AC current from wall outlets to DC current PC uses.
Electricity measure in amps, volts, ohms, watts.
Multimeters consist of analog or digital display, two probes, function selector switch.
Main protection against ESD is use of antistatic wrist straps and ESD mats. Other techniques include antistatic bags, humidity control, antistatic spray.

## Slide 39: Summary
Three main types of power problems: Power quality problems (EMI, RFI); power overage problems (spikes, surges); and power undervoltage problems (sags, brownouts, blackouts).
Solutions to power problems include line conditioners, surge protectors, and backup power supplies (SPSs and UPSs).

## Slide 40: Summary
Power supplies rated in watts, provide standard voltages (3.3V, +5V, -5V, +12V, -12V) to motherboard and drives. Common form factors today are Baby AT, ATX, ATX 12V.
Common PSU power connectors: Floppy drive (Berg), standard peripheral (Molex); motherboard connectors (P8/P9, P1, P4).
Power supply should provide at least 10% more power than PC system components require.

## Slide 41: Summary
When installing PSU, ensure it is set for correct input voltage (110V in U.S.).
You can tell power supply is functioning if you hear PSU fan.
When troubleshooting PSU, check wall outlet, power cord, power switch, power strips, voltage switch, motherboard connectors.

## Slide 42: Key Terms
Alternating current (AC)
Amps
Antistatic bag
Antistatic wrist strap
Auto-ranging multimeter
Berg connector
Brownout
Capacitor
Circuit
Conductor
Continuity
Current
Cutover threshold
Direct current (DC)
Electromagnetic interference (EMI)

## Slide 43: Key Terms
Electrostatic discharge (ESD)
ESD mat
EST wrist strap
Floppy drive power connector (Berg connector)
Insulator
Line conditioner
Line power
Molex connector
Multimeter
Ohms
Power
Radio frequency interference (RFI)
Resistance
Resistor

## Slide 44: Key Terms
Sag
Spike
Standard peripheral power connector (Molex)
Standby power supply (SPS)
Surge
Surge protector
Uninterruptible power supply (UPS)
Voltage
Volts
Watts

## Slide 45: Copyright Notice
Copyright 2008 John Wiley & Sons, Inc. All rights reserved. Reproduction or translation of this work beyond that permitted in section 117 of the 1976 United States Copyright Act without express permission of the copyright owner is unlawful. Requests for further information should be addressed to the Permissions Department, John Wiley & Sons, Inc. The purchaser may make back-up copies for his/her own use only and not for distribution or resale. The Publisher assumes no responsibility for errors, omissions, or damages caused by the use of these programs or from the use of the information herein.